## Slide 1: EE 445L – Embedded System Design Lab
Lab 3
Edge Triggered Interrupts
Time delay interrupt
EdgeInterruptDebounce_4C123

## Slide 2: Lab 3
  Develop a graphics driver for the LCD that can plot lines and circles
  Design a hardware/software interface for a keyboard or individual switches
  Design a hardware/software driver for generating a simple tone on a speaker
  Measure supply current necessary to run the embedded system
  Implement a digital alarm clock using periodic interrupts

## Slide 3: TM4C Interrupt Vectors
77 interrupt sources on TM4C123 with 8 priority levels
Vector address | Num | IRQ | ISR | NVIC | Priority bits
0x0000003C | 15 | -1 | SysTick Handler | NVIC_SYS_PRI3_R | 31 – 29
0x00000040 | 16 | 0 | GPIO Port A | NVIC_PRI0_R | 7 – 5
0x00000044 | 17 | 1 | GPIO Port B | NVIC_PRI0_R | 15 – 13
0x00000048 | 18 | 2 | GPIO Port C | NVIC_PRI0_R | 23 – 21
0x0000004C | 19 | 3 | GPIO Port D | NVIC_PRI0_R | 31 – 29
0x00000050 | 20 | 4 | GPIO Port E | NVIC_PRI1_R | 7 – 5
0x00000054 | 21 | 5 | UART0 Rx/Tx | NVIC_PRI1_R | 15 – 13
0x00000058 | 22 | 6 | UART1 Rx/Tx | NVIC_PRI1_R | 23 – 21
0x0000008C | 35 | 19 | Timer 0A | NVIC_PRI4_R | 31 – 29
0x00000090 | 36 | 20 | Timer 0B | NVIC_PRI5_R | 7 – 5
0x00000094 | 37 | 21 | Timer 1A | NVIC_PRI5_R | 15 – 13
0x00000098 | 38 | 22 | Timer 1B | NVIC_PRI5_R | 23 – 21
0x0000009C | 39 | 23 | Timer 2A | NVIC_PRI5_R | 31 – 29
0x000000A0 | 40 | 24 | Timer 2B | NVIC_PRI6_R | 7 – 5
0x000000B8 | 46 | 30 | GPIO Port F | NVIC_PRI7_R | 23 – 21

## Slide 4: Things That Must Be Done In An Interrupt Initialization Ritual
Turn on clock for the device
Initialize any data structures
Arm (specify a flag may interrupt)
Activate (NVIC)
Set priority
Enable (allow all interrupts in main)

## Slide 5: Rising Edge Counter Interrupt Ritual
void Switch_Init(void(*touchtask)(void), void(*releasetask)(void)){
SYSCTL_RCGCGPIO_R |= 0x00000020; // (a) activate clock for port F
while((SYSCTL_PRGPIO_R & 0x00000020) == 0){};
GPIO_PORTF_DIR_R &= ~0x10; // (c) make PF4 in (built-in button)
GPIO_PORTF_DEN_R |= 0x10; // enable digital I/O on PF4
GPIO_PORTF_PUR_R |= 0x10; // enable weak pull-up on PF4
GPIO_PORTF_IS_R &= ~0x10; // (d) PF4 is edge-sensitive
GPIO_PORTF_IBE_R |= 0x10; // PF4 is both edges
GPIOArm();
SYSCTL_RCGCTIMER_R |= 0x01; // 0) activate TIMER0
TouchTask = touchtask; // user function
ReleaseTask = releasetask; // user function
Touch = 0; // allow time to finish activating
Release = 0;
Last = PF4; // initial switch state
}

## Slide 6: When a Port F interrupt is triggered…
The current instruction is finished
Eight registers are pushed on the stack with R0 on top
  pushed onto whichever stack is active: either the MSP or PSP
The vector address is loaded into the PC
The ISPR register is set to 46 (Port F)
The top 24 bits of LR are set to 0xFFFFFF, and the bottom four bits:
  0xF1 Return to Handler mode MSP (if interrupt of an ISR)
  0xF9 Return to Thread mode MSP
  0xFD Return to Thread mode PSP
We will use this
0xE9 means floating point

## Slide 7: When a Port F interrupt is triggered…

## Slide 8: Things That Must Be Done In An Interrupt Service Routine
ISR must do one of these two:
  Acknowledge (clear trigger flag)
  Disarm
Communicate via shared globals to other threads
  Semaphore flag
  FIFO queue

## Slide 9: Rising Edge Counter Interrupt Service Routine
void GPIOPortF_Handler(void){
GPIO_PORTF_IM_R &= ~0x10; // disarm PF4
if(Last){ // 0x10 means it was previously released
Touch = 1; // touch occurred
(*TouchTask)(); // execute user task
}
else{
Release = 1; // release occurred
(*ReleaseTask)(); // execute user task
}
Timer0Arm(); // start one shot
}

## Slide 10: Rising Edge Counter Interrupt Service Routine
void Timer0A_Handler(void){
TIMER0_IMR_R = 0x00000000; // disarm timeout
Last = PF4; // switch state
GPIOArm(); // start GPIO
}
static void GPIOArm(void){
GPIO_PORTF_ICR_R = 0x10; // clear flag4
GPIO_PORTF_IM_R |= 0x10; // arm interrupt on PF4
NVIC_PRI7_R = (NVIC_PRI7_R&0xFF00FFFF)|0x00A00000; // 5
NVIC_EN0_R = 0x40000000; // enable interrupt 30 in NVIC
}

## Slide 11: Critical Sections – Nonreentrant Code
Shared access to permanently allocated data or I/O port
Multistep non-atomic sequence, in which one step is a write:
  Read modify write
  Write write
  Write read

## Slide 12: Summary
Arm, enable, disable
Priority
Vector
LR = 0xFFFFFFF9
Debounce
Latency
Critical section