## Slide 1: EE 445L – Embedded System Design Lab
Critical Sections
Reentrant Code
Labs 2,3

## Slide 2: Critical Section
void main(void){
while(1){
GPIO_PORTF_DATA_R ^= 0x02;
}
}
Loop LDR r0,[pc,#32]
LDR r0,[r0,#0x00]
EOR r0,r0,#0x02
LDR r1,[pc,#20]
STR r0,[r1,#0x3FC]
B Loop
void ISR1(void){
GPIO_PORTF_DATA_R ^= 0x04;
Stuff1();
}
ISR1 ...
LDR r1,[pc,#56]
LDR r0,[r1,#0x00]
EOR r0,r0,#0x04
LDR r1,[pc,#52]
STR r0,[r1,#0x3FC]
...
Shared global
Nonatomic access
At least one write
Show project in Keil
Solution: remove sharing

## Slide 3: Critical Section
void main(void){
...
while(1){
Display(Hour);
Display(Minute);
}
}
void ISR1(void){
Second++;
if(Second==60){
Second = 0;
Minute++;
if(Minute == 60){
Minute = 0;
Hour++;
}
}
}
Shared global
Nonatomic access
At least one write
Lab 3

## Slide 4: Critical Section
void main(void){
...
while(1){uint32_t myH,myM;
Disable_Interrupts();
myH = Hour; myM = Minute;
Enable_Interrupts();
Display(myH);
Display(myM);
}
}
void ISR1(void){
Second++;
if(Second==60){
Second = 0;
Minute++;
if(Minute == 60){
Minute = 0;
Hour++;
}
}
}
Shared global
Nonatomic access
At least one write
Solution: make atomic
Lab 3

## Slide 5: Critical Section
void main(void){
...
while(1){uint32_t myT;
myT = Time;
Display(myT/100);
Display(myT%100);
}
}
void ISR1(void){
Second++;
if(Second==60){
Second = 0;
Minute++;
if(Minute == 60){
Minute = 0;
Hour++;
}
} Time = 100*Hour+Minute;
}
Shared global
Nonatomic access
At least one write
Solution: make atomic
Lab 3

## Slide 6: Reentrant Code
int PutFifo(int32_t data){
if(((PutI+1)%SIZE) == GetI){
return 0;
}
FIFO[PutI] = data;
PutI = (PutI+1)%SIZE;
return 1;
}
void GPIOPortA_Handler (void){
PutFifo(GPIO_PORTA_DATA_R);
}
Solution: Use local variables?
void GPIOPortB_Handler (void){
PutFifo(GPIO_PORTB_DATA_R);
}
Function call by two threads
Recursion

## Slide 7: Reentrant Code
int PutFifo(int32_t data){long sr;
sr = StartCritical();
if(((PutI+1)%SIZE) == GetI){
EndCritical(sr);
return 0;
}
FIFO[PutI] = data;
PutI = (PutI+1)%SIZE;
EndCritical(sr);
return 1;
}
void GPIOPortA_Handler (void){
PutFifo(GPIO_PORTA_DATA_R);
}
Function call by two threads
Solution: Atomic access to globals
void GPIOPortB_Handler (void){
PutFifo(GPIO_PORTB_DATA_R);
}

## Slide 8: Summary
Critical sections
  Shared global
  Non-atomic access
  At least one write
Solution: remove sharing
  Bit-specific access to Ports
Solution: make atomic
  Disable interrupts during critical section
  Pack data into a single 32-bit variable