## Slide 1: EE 445L – Embedded System Design Lab
Sound Generation
Music
For more information read sections 8.4, 9.2.2

## Slide 2: Audio
Frequency defines pitch
Humans hearing ~ 25 - 20,000 Hz
  most sensitive to sounds in the 1 – 5 kHz range
Sound intensity level
  LI = 10log10|I|/I0; I0 = 10-12 Watt/m2
  A whisper = 15 dB
  Normal conversation = 60 dB
  A lawnmower = 90 dB
  A car horn = 110 dB
  A rock concert or a jet engine = 120 dB
  A gunshot or firecracker = 140 dB

## Slide 3: Music
a Note has five parameters
    Amplitude (loudness)
    Frequency (pitch)
    Voice (shape)
    Envelope (time varying shape)
    Duration
middle A is 440 Hz
relation of frequency of other notes:
  Note frequency = 440 *2N/12Hz
  where "N" is number of notes up or down from middle A
middle C is 261.6 Hz
music contains multiple harmonics

## Slide 4: Music
music contains multiple harmonics

## Slide 5: Sine wave generation
Chart: 12-bit sin table
Tone generated from 256 discrete 12-bit outputs
SNR = 20log10(signal/noise)
Signal and noise measured in volts, SNR in dB
5 bits is 20log10(32) = 30 dB
8 bits is 20log10(256) = 48 dB
10 bits is 20log10(1024) = 60 dB
12 bits is 20log10(4096) = 72 dB
Number of bits
DAC precision
Buffer size
Output one value to DAC
Timer ISR

## Slide 6: 523 Hz sine wave output 12-bit DAC
6
32 outputs 256 outputs
31 dB ≈ 35 to 1 ratio 49 dB ≈ 281 to 1 ratio
SNR = 31 dB (3dB – -28dB)
SNR = 49 dB (3dB – -46dB)

## Slide 7: Musical Notes

## Slide 8: Tone Generation
Sample rate
  440 Hz tone
  80 MHz clock (12.5 ns interval)
  64 points/sinusoid period
  (80Mcounts/s/440Hz)/64 points = 2841 counts = 35.5 us/point
  if 256 points/period  8.9 us/point

## Slide 9: Tone Generation
uint32_t I;
// 11-bit 64-element sine wave
const uint16_t Wave[64] = {
1024,1122,1219,1314,1407,1495,1580,1658,1731,1797,1855,
1906,1948,1981,2005,2019,2024,2019,2005,1981,1948,1906,
1855,1797,1731,1658,1580,1495,1407,1314,1219,1122,1024,
926,829,734,641,553,468,390,317,251,193,142,
100,67,43,29,24,29,43,67,100,142,193,
251,317,390,468,553,641,734,829,926
};
TIMER0_TAILR_R = 2841; // 35.5125us, 439.9859Hz
void Timer0A_Handler(void){
TIMER0_ICR_R = TIMER_ICR_TATOCINT;// acknowledge
I = (I+1)&0x3F; // 0 to 63
DAC_Out(Wave[I]);
}
Why 11 bits?
Output one value to DAC
Timer ISR

## Slide 10: Tone Generation
EE 445L – Bard, Valvano
Combining two tones:
  1) Reduce range of each to 11 bits, 0 to 2047
  2) Use two timer interrupts, one for each wave
  3) Maintain two indices I0 and I1
  4) Add the waveforms together in both ISRs

## Slide 11: Tone Generation
Design data structures for musical information
  voltage versus time (the sin wave)
  timer delays for each note in a scale (pitch)
  song table (voice, pitch, duration)
    songs divided into measures
  pauses between notes
    constant DAC input

## Slide 12: Song Generation
a Note is defined by five parameters
    Amplitude (loudness)
    Frequency (pitch)
    Voice (shape)
    Envelope (time varying shape)
    Duration

## Slide 13: Envelope
Each different type instrument has unique tone qualities
a Note is defined by five parameters
    Amplitude (loudness)
    Frequency (pitch)
    Voice (shape)
    Envelope (time varying shape)
    Duration

## Slide 14: Summary
SNR = 20log10(signal/noise)
  DAC resolution
  Frequency resolution
Sound
  Amplitude (loudness)
  Frequency (pitch)
  Voice (shape)
  Envelope (time varying shape)
  Duration
For more information read sections 8.4, 9.2.2