## Slide 1: EE 445L – Embedded System Design Lab
Data flow graphs
Processor
Architecture
Interfaces
Reading assignment: Chapters 1, 2 & 3

## Slide 2: Data Flow Graph
Lab 3 Alarm clock
Circles
Software components
Rectangles
Hardware components
Systems
Components
Interfaces
Arrows
Data format
Data bandwidth
Data direction
For more information read Section 1.3.3 in the book

## Slide 3: Motor Controller Data Flow Graph
Arrows
Data format
Data bandwidth
Data direction
Circles
Software components
Rectangles
Hardware components
Lab 10 Integral Controller

## Slide 4: Memory Mapped Processor Architecture
 | TM4C123
0x0000.0000 | 256 KiB
∙∙∙ | Flash
0x0003.FFFF | ROM
0x2000.0000 | 32 KiB
∙∙∙ | Static
0x2000.7FFF | RAM
Harvard Architecture
RISC

## Slide 5: Cortex M4 Block Diagram

## Slide 6: Cortex M RISC Architecture
For more information read Sections 2.1 and 2.3 in the book
Few instructions
Fixed lengths
Execute in 1 or 2 cycles,
Only load and store can access memory,
No one instruction can both read and write memory
Many GP registers
Few addressing modes

## Slide 7: Cortex M Architecture
APSR contains the current state of the condition
flags from previous instruction executions
IPSR contains the exception type number of the
current Interrupt Service Routine (ISR)
EPSR contains the Thumb state bit and the execution
state bits for the If-Then (IT) instruction

## Slide 8: TI Microcontrollers
Launch Pad
Connected LaunchPad
For more information read Sections 2.1-2.4 in the book
 | TM4C123
0x0000.0000 | 256 KiB
∙∙∙ | Flash
0x0003.FFFF | ROM
0x2000.0000 | 32 KiB
∙∙∙ | Static
0x2000.7FFF | RAM

## Slide 9: TM4C123 Memory Map

## Slide 10: Bit Banding Example
0x00000000
0x00000000
0000_0000_0000_0000_0000_0000_0001_0000
RAM Address [0x2000_0000]
0x00000000
0x00000001
0x00000000
0x00000000
0x00000000
0x00000000
[0x2200001C]
[0x22000018]
[0x22000014]
[0x22000010]
[0x220000C]
[0x22000008]
[0x22000004]
[0x22000000]
RAM Value: 0x0000_0010
Bit Banded RAM Addresses
BB DATA:
bit_word_offset = (byte_offset x 32) + (bit_number × 4) bit_word_offset = 0 x 32 + 4 x 4 = 0x10
bit_word_addr = bit_band_base + bit_word_offset bit_word_addr = 0x2200_0000 + 0x10 = 0x2200_0010

## Slide 11: I/O Port Bit Specific Addressing
I/O Port bit banding used to access port data register
  Define address offset as 4*2b, where b is the selected bit position
  256 possible bit combinations (0-8)
  Add offsets for each bit selected to base address for the port
  Example: Port A, bits 1,2,3
Port A = 0x4000.4000
PA321 =
0x4000.4000+0x0008+0x0010+0x0020
= 0x4000.4038
Provides friendly and atomic access to port pins
These base addresses are different on the TM4C1294

## Slide 12: Little endian memory access

## Slide 13: Embedded System Architecture
For more information read Section 1.1 in the book

## Slide 14: Introduction to Interfacing
An interface:
  is the hardware and software that combine to allow the computer to communicate with external hardware
  it must be able to adapt to a wide range of inputs and outputs that can exist in either digital analog or time form
For more information read Sections 2.2 and 2.4 in the book

## Slide 15: TM4C123 Architecture
For more information read Section 2.2.1 in the book

## Slide 16: Interfaces
Universal Asynchronous Receiver Transmitter
  UART
  Serial means one bit at a time
  Interaction between PC running PuTTy
  Microcontroller network, Lab 4 CC3100
ADC
  12-bit precision
  0 to 3.3V range

## Slide 17: Interfaces
The Synchronous Serial Interface (SSI)
  Shift registers
  Organic Light Emitting Diode (OLED)
  ST7735R Liquid Crystal Display (LCD)
  Analog to Digital Converters (ADC)
  Digital to Analog Converters (DAC)
  Other microprocessors

## Slide 18: Interfaces
The timer features on the TM4C:
  Fixed periodic rate interrupts
  Pulse Width Modulated outputs (PWM)
  Event counter system for advanced timing operations
  Input capture used for period and pulse width measurement
  Output compare used for generating signals and frequency measurement

## Slide 19: Summary
Data Flow Graph
Microcontroller
RISC processor
Little endian memory
Introduction to interfacing
  Digital
  Serial
  Analog
  Time