## Slide 1: EE 445L – Embedded System Design Lab
I/O synchronization
Blind
Busy-wait
Interrupts
DMA

## Slide 2: Input/Output Synchronization
Timing Mismatch
  Processor ~ MHz
  Peripheral ~ KHz or Hz
Respond to events
  Periodic tasks: ADC, DAC, control systems
  Aperiodic tasks: input, output, alarms

## Slide 3: I/O SYNCHRONIZATION

## Slide 4: INPUT SYNCHRONIZATION

## Slide 5: OUTPUT SYNCHRONIZATION

## Slide 6: Busy-Wait Conditions
Predicable
Simple I/O
Fixed load
Dedicated, single thread
Single process
Nothing else to do

## Slide 7: Interrupt Conditions
Variable arrival times
Complex I/O, different speeds
Variable load
Other functions to do
Multithread or multiprocess
Infrequent but important alarms
Program errors
Overflow, invalid op code
Illegal stack or memory access
Machine errors
Power failure, memory fault
Breakpoints for debugging
Real time clocks
Data acquisition and control

## Slide 8: Direct Memory Access (DMA)
Low latency
High Bandwidth
DMA Examples on web site
  DMASoftware_xxx.zip – memory to memory transfer
  DMASPI_xxx.zip – memory to DAC continuous output
  DMATimerPortRead_xxx.zip – timer-triggered GPIO to memory
  DMATimerPortWrite_xxx.zip – timer-triggered memory to GPIO

## Slide 9: Interrupts
An interrupt is the automatic transfer of software execution in response to hardware that is asynchronous with current software execution.
  external I/O device (like a keyboard or printer) or
  an internal event (like an op code fault, or a periodic timer.)
  occurs the hardware needs service (busy to done state transition)

## Slide 10: Interrupt Processing
All interrupting systems must have the
  ability for the hardware to request action from computer
  ability for the computer to determine the source of the request
  ability for the computer to acknowledge the interrupt

## Slide 11: Multiple Devices busy-wait synchronization
Bandwidth can be improved by establishing concurrent I/O operations

## Slide 12: Summary
Synchronization
Blind
Busy-wait
Interrupts
DMA
EE 445L – Bard, McDermott, Valvano