## Slide 1: EE 445L – Embedded System Design Lab
Digital logic
Bipolar Junction Transistor (BJT)
MOS Field Effect Transistor (MOSFET)
Effect of capacitance
Buzzer

## Slide 2: Digital Logic (MOS-MOS) Output High State
The device providing (driving) the output is capable of sourcing a maximum current to that output
  IOH
Each input device receiving (sinking) the output as an input requires a maximum current:
  IIH
For more information read Section 1.4 in the book

## Slide 3: Digital Logic (MOS-MOS) Output Low State
The device providing (driving) the output is capable of receiving (sinking) a maximum current through the output
  IOL
Each input device sources a maximum current:
  IIL

## Slide 4: Digital Logic (MOS-TTL(BJT)) Output High State
The device providing (driving) the output is capable of sourcing a maximum current to that output
  IOH
Each input device receiving (sinking) the output as an input requires a maximum current:
  IIH
For more information read Section 1.4 in the book

## Slide 5: Digital Logic (MOS-TTL(BJT)) Output Low State
The device providing (driving) the output is capable of receiving (sinking) a maximum current through the output
  IOL
Each input device sources a maximum current:
  IIL

## Slide 6: Digital Logic Families
The following five parameters most affect our choice of logic families:
  power supply voltage
  power supply current
  speed
  output drive, IOL, IOH
  noise immunity

## Slide 7: Digital Logic Families
Logic voltage levels
  VIL – voltage below which an input is considered logic low
  VIH - voltage above which an input is considered logic high
  VOH – output voltage for a logic high (current less than IOH)
  VOL - output voltage for a logic low (current less than IOL)
VOL £ VIL
VOH ³ VIH

## Slide 8: Logic Families
Family | Example | IOH | IOL | IIH | IIL
Standard TTL | 7404 | 0.4 mA | 16 mA | 40 µA | 1.6 mA
Schottky TTL | 74S04 | 1 mA | 20 mA | 50 µA | 2 mA
Low Power Schottky | 74LS04 | 0.4 mA | 4 mA | 20 µA | 0.4 mA
High Speed CMOS | 74HC04 | 4 mA | 4 mA | 1 µA | 1 µA
Adv High Speed CMOS | 74AHC04 | 4 mA | 4 mA | 1 µA | 1 µA
TM4C 2mA-drive | TM4C123 | 2 mA | 2 mA | 2 µA | 2 µA
TM4C 4mA-drive | TM4C123 | 4 mA | 4 mA | 2 µA | 2 µA
TM4C 8mA-drive | TM4C123 | 8 mA | 8 mA | 2 µA | 2 µA
TM4C 12mA-drive | TM4C1294 | 12 mA | 12 mA | 2 µA | 2 µA
For more information read Section 1.4 in the book

## Slide 9: Digital Logic Families
VOH ³ VIH
IOH ³ IIH

## Slide 10: Digital Logic Families
VOL £ VIL
IOL ³ IIL

## Slide 11: Digital Logic Families
VOH ³ VIH
IOH ³ IIH
VOL £ VIL
IOL ³ IIL

## Slide 12: NPN Transistor Model
1) Normally Vc > Ve
2) Current can only flow in the following directions
  from base to emitter (input current)
  from collector to emitter (output current)
  from base to collector
    (doesn’t usually happen, but could if Vb > Vc)
3) Each transistor has maximum values that should not be exceeded
  Ib Ic Vce and Ic•Vce
4) The transistor acts like a current amplifier
  Ic = hfe•Ib
5) The transistor will saturate if Vb > Ve + Vbe(SAT)
  where Vbe(SAT) is typically above 0.6V
For more information read Section 1.4 in the book
PN2222 Lab 3
TIP120 Lab 10
Reverse active
Cutoff
Saturation
Forward active
VBE
VBC
E < B < C
E < B > C
E > B < C
E > B > C

## Slide 13: Transistors
Type | NPN | PNP | package | Vbe(SAT) | Vce(SAT) | hfe min/max | Ic
general purpose | 2N3904 | 2N3906 | TO-92 | 0.85 V | 0.2 V | 100 | 10mA
general purpose | PN2222 | PN2907 | TO-92 | 1.2 V | 0.3 V | 100 | 150mA
general purpose | 2N2222 | 2N2907 | TO-18 | 1.2 V | 0.3 V | 100/300 | 500mA
power | TIP29A | TIP30A | TO-220 | 1.3 V | 0.7 V | 15/75 | 1A
power | TIP31A | TIP32A | TO-220 | 1.8 V | 1.2 V | 25/50 | 3A
power | TIP41A | TIP42A | TO-220 | 2.0 V | 1.5 V | 15/75 | 3A
Darlington | TIP120 | TIP125 | TO-220 | 2.5 V | 2.0 V | 1000 min | 3A
PN2222 Lab 3
TIP120 Lab 10

## Slide 14: Lab 3 Speaker Interface
2.25" 32 OHM SPEAKER - 0.38" thick
Resistor, R, controls loudness
Power = V*I

## Slide 15: Lab 3 Speaker Interface
Assume TM4C output at 3.3V
At saturation (maximum loudness)
  VBE = 1.2V and VCE = 0.3V
Ohms Law across speaker
  ICE = (3.3-0.3V)/32W = 94mA (near maximum!)
  P = ICE2*32W = 0.28 watts (too loud)
Transistor gain is 100
  IB =ICE /100 = 1mA
Ohms Law across input resistor
  R = (3.3-1.2V)/0.001A = 2000W
What if R = 10kW?
  IB =(3.3-1.2V)/10000W = 0.21mA
  hie = 2kW (not a fixed value)
  IB =VOH/(R +hie) =3.3V/(10000W +2000W)= 0.28mA
Transistor gain is 100
  ICE =IB *100 = 21mA
  P = ICE2*32W = 0.015 watts
  quiet
Use data sheet to guess
Measure with voltmeter

## Slide 16: Capacitance
Capacitance loading is an important factor when interfacing CMOS devices
Make it run faster
  Decrease R,C
  Increase I, P
Make it less noisy
  Decrease slew rate

## Slide 17: Take Aways
R - Resistive loads require current amplification
L - Inductive loads produce back EMF
  Snubber diode
C - Capacitive loads will slow down dV/dt
  Time constant, t = R*C
Make it go faster by
  Decreasing R and C
  Increasing I
Speed related to power

## Slide 18: Summary
Saturated Mode
Current gain hfe
Activation Vbe
Output Vce Ice
Capacitance
  Slows down
  Reduces EM emissions